## Cycle Sign-off Certificate
To be completed after cycle-build or expiration of previous sign-off.
Make:	Model:	Colour:	Size:

### Torque Settings Checks
ITEM	TORQUE SETTING (Nm)	Checked?
Front Wheel Nuts
Rear Wheel Nuts
Headset Retaining bolts / threaded nut
Stem / Handlebar bolts.
Brake / Gear lever bolts.
Pedals
Crank Arm bolts / locknuts
Seat post clamp
Seat clamp
Front and rear derailleur bolts
Rack bolts
Front Brake mounting bolts
Front Brake Caliper bolts (disc split pin)
Rear Brake mounting bolts
Rear Brake Caliper bolts (disc split pin)

### Additional Checks
ITEM	Checked?
Sharp edges, handlebar end caps, cable ends.
Frame alignment, fork alignment, tracking
Cables and wiring secured.
Braking: performance, calibration and ease of use
Steering: ease of use, smooth, stem security and feel.
Wheel Truth, 2mm run-out permissible.
Wheel bearings smooth, no shake.
Rim wear. Rims to be stable at type 30% over-pressure.
Spokes all in good condition and tight
Tyre condition, sides, tread and pressure.
Drivetrain: Chain check, derailleur check, gear-shifting check.
Pedal alignment and BB shake.
Saddle: security and tilt.
Lighting: rear reflector+lamp, front lamp (and reflector for dynamos systems). Amber reflectors on pedals.
Bell, ringing and secured.

List any other accessories below:	Checked?

This cycle has been checked according to the CTC Hire Standard, available at cycling.org, and deemed suitable for use by the pubic by the following qualified mechanic:

Signature:………………………………………….	Date…………………………………..

Print Name:………………………………………..	Valid for ………… calendar months